## Slide 1: Design of a Phase Locked Loop (PLL) Circuit
Shirazush Salekin Chowdhury
PhD Student
Bradley Department of Electrical and Computer Engineering
Virginia Tech

## Slide 2: Outlines
PLL Introduction
[Pages: 3 to 12]
Condition for the locked/steady state
[Page: 13]
Discussion on the PLL Design (Mostly Theoretical)
[Pages: 14 to 58]
Phase Frequency Detector
Charge Pump and Loop Filter
Voltage Controlled Oscillator
Divider Circuits
Whole Circuit Schematic and Layout example
Results
Step by Step Design Guide of PLL in Cadence
[Pages: 59 to 88]
References
[Page: 89]
Note: For a better understanding of the concepts, please use slideshow mode, as it includes helpful graphics!

## Slide 3: INTRODUCTION
Feedback Control Circuit
Frequency and Phase of
                 output signal ∝ Input Signal
Forward Loop Gain
FIN,Ref = 200 MHz
FOUT = 200 x 8 MHz
= 1600 MHz
÷ 8
FFB = 1600 ÷ 8
= 200 MHz
÷ 4
FFB = 800 ÷ 4
= 200 MHz
FOUT = 200 x 4 MHz
= 800 MHz
Simplify and let’s call it “Forwards Loop Gain”

## Slide 4: Why Do We Need PLL?
To Synthesize Frequency from a Master Clock
Master Clock
 LC Circuit
 Crystal Oscillator

## Slide 5: Why Do We Need PLL?

## Slide 6: Why Do We Need PLL?

## Slide 7: Crystal Oscillator
Limitations:
 Output frequency is low
 Very limited tunability after fabrication
 Large area
OUR REQUIREMENTS!
 Tunable
 High Frequency
 Periodic Signal Generator

## Slide 8: Why Do We Need PLL?
Wireless System
 Generation of carrier frequency, FLO to
 To upconvert baseband signal into passband signal in TX
 To downconvert passband signal into baseband signal in RX

## Slide 9: Why Do We Need PLL?
Wireless System
 Generation of carrier frequency, FLO to
 To upconvert baseband signal into passband signal in TX
 To downconvert passband signal into baseband signal in RX
Wireline Application
 Transmit bits every clock period
 Fast data transfer rate
Analog Systems
 Sampling the analog signals in ADCs
 Tunable digital filter using switch capacitor

## Slide 10: BLOCK DIAGRAM
Basic block diagram of PLL :
PLL
Output
signal
Input
signal
FREF = ω0 MHz
FOUT = ω0 MHz
FFB = FOUT = ω0 MHz

## Slide 11: BLOCK DIAGRAM
Basic block diagram of PLL :
PLL
Output
signal
Input
signal
FREF = ω0 MHz
FOUT = ω0 x N MHz
FFB = ω0/N MHz
Frequency Divider
÷ N

## Slide 12: BLOCK DIAGRAM
Basic block diagram of PLL :
Phase Detector
(PD)
Voltage Controlled Oscillator
(VCO)
Low Pass Filter
(LPF)
Output
signal
Input
signal
Vin
Vout
Ve
Vc
φin
φout
φer
φer(t)= φin(t) - φout(t)
Ve ∝ φer(t)
Vin = Ain sin (ωin t); φin = ωin t
Vout = Aout cos (ωout t); φout = ωout t
Ve Vc (Low f components)
Filtered
Loop Filter
Output of PD, Ve ∝ φer
ωout ∝ Vc

## Slide 13: Condition for the locked/steady state
Basic block diagram of PLL :
Phase Detector
(PD)
Voltage Controlled Oscillator
(VCO)
Low Pass Filter
(LPF)
Output
signal
Input
signal
Vin
Vout
Ve
Vc
φin
φout
φer
ωin = ωout
i.e. constant

## Slide 14: Simple Implementation of a PLL
Phase (Error) Detector: PD
Phase Detector
(PD)
Voltage Controlled Oscillator
(VCO)
Low Pass Filter
(LPF)
Output
signal
Input
signal
Vin
Vout
Ve
Vc
φin
φout
φer
Phase Detector
(PD)
Recall: We want to find the phase error, φer(t)= φin(t) - φout(t)
But How?
Trigonometry
 Product to Sum Identities

## Slide 15: Phase (Error) Detector: PD
Mixer
Vin
Vout
Ve
Mixer:
 Combines two or more input signals, Vin and Vout
 Produces an output signal
 Contains the sum and difference frequencies of the input signals
Ve ∝ Vin + Vout OR
Ve ∝ Vin - Vout
Trigonometry
 Product to Sum Identities
 sin A cos B = ½ sin (A+B) + sin (A-B)
Vin = Ain sin (ωin t)
Vout = Aout cos (ωout t)
Vin Vout = Ain sin (ωin t) x Aout cos (ωout t)
= ½ Ain Aout sin (ωin + ωout) t + sin (ωin - ωout) t

## Slide 16: Phase (Error) Detector: PD
Mixer
Vin
Vout
Ve
Cases:
#1: Freq = No error and φ = No error
 Δω = ωin - ωout = 0
 ωin = ωout = ω
 φer = 0
#2: Freq = error and φ = No error
 ωin = ω
 ωout = ω - Δω
 φer = 0
#3: Freq = No error and φ = error
 Δω = ωin - ωout = 0
 ωin = ωout = ω
 φer ≠ 0

## Slide 17: Phase (Error) Detector: PD
Mixer
Vin
Vout
Ve
Case #1: Freq = No error and φ = No error
 Δω = ωin - ωout = 0
 ωin = ωout = ω
 φer = 0
Ve=Vin Vout = ½ Ain Aout sin (ωin + ωout) t + sin (ωin - ωout) t
= ½ Ain Aout sin (ω + ω) t + sin (ω - ω) t
= ½ Ain Aout sin 2ω t + sin (0)
= ½ Ain Aout sin 2ω t
We only have the high- frequency component

## Slide 18: Phase (Error) Detector: PD
Mixer
Vin
Vout
Ve
Case #2: Freq = error and φ = No error
 ωin = ω
 ωout = ω - Δω
 φer = 0
Ve=Vin Vout = ½ Ain Aout sin (ωin + ωout) t + sin (ωin - ωout) t
= ½ Ain Aout sin (ω + ω - Δω) t + sin (ω - ω + Δω) t
= ½ Ain Aout sin (2ω – Δω) t + sin (Δω)t
Ve ∝ frequency error, Δω
High frequency component

## Slide 19: Phase (Error) Detector: PD
Case #3: Freq = No error and φ = error
 Δω = ωin - ωout = 0
 ωin = ωout = ω
 φer ≠ 0
 φer (0) = φin (0) - φout (0)
Vin = Ain sin (ωin t + φin (0))
Vout = Aout cos (ωout t+ φout (0))
Ve=Vin Vout = ½ Ain Aout sin (ωin + ωout) t + sin (ωin - ωout) t
= ½ Ain Aout sin (ω+φin (0) + ω+ φout (0)) t + sin (φer (0)) t
= ½ Ain Aout sin (2ω+φin (0) + φout (0)) t + sin (φer (0)) t
Ve has two components:
 @ 2ω frequency
 @ DC

## Slide 20: Phase (Error) Detector: PD Summary
Cases:
#1: Freq = No error and φ = No error
#2: Freq = error and φ = No error
#3: Freq = No error and φ = error
Ve=Vin Vout = ½ Ain Aout sin 2ω t
Ve=Vin Vout = ½ Ain Aout sin (2ω – Δω) t + sin (Δω)t
Ve=Vin Vout = ½ Ain Aout sin (2ω+φin (0) + φout (0)) t + sin (φer (0)) t
We only have the high- frequency component
Ve ∝ frequency error, Δω
Ve has two components:
 @ 2ω frequency
 @ DC

## Slide 21: Phase (Error) Detector: PD Summary
Low Pass Filter
(LPF)
Ve
Vc
φer
R
C
Ve
φer
Vc
Ve=Vin Vout = ½ Ain Aout sin 2ω t
Ve=Vin Vout = ½ Ain Aout sin (2ω – Δω) t + sin (Δω)t
Ve=Vin Vout = ½ Ain Aout sin (2ω+φin (0) + φout (0)) t + sin (φer (0)) t

## Slide 22: Filters

## Slide 23: Frequency Spectrum of the Ve signal
ωc =
ƒc =
Low Pass Filter
(LPF)
Ve
Vc
φer
R
R
C
Ve
φer
Vc

## Slide 24: Frequency Spectrum of the Ve signal
2ω
ω-3dB
BW
Ve(dB)
ω
Ve=Vin Vout = ½ Ain Aout sin 2ω t
We only have the high- frequency component
Case #1:

## Slide 25: Frequency Spectrum of the Ve signal
2ω – Δω
ω-3dB
BW
Ve(dB)
ω
Ve=½ Ain Aout sin (2ω – Δω) t + sin (Δω)t
Case #2:
Ve ∝ frequency error, Δω
Δω

## Slide 26: Frequency Spectrum of the Ve signal
2ω+φin (0) + φout (0)
ω-3dB
BW
Ve(dB)
ω
Ve= ½ Ain Aout sin (2ω+φin (0) + φout (0)) t + sin (φer (0)) t
Case #3:
2nd component
sin (φer (0)
DC, since ω = 0
-3dB

## Slide 27: BLOCK DIAGRAM
Basic block diagram of PLL (frequency synthesizer) :

## Slide 28: BLOCK DIAGRAM
Basic block diagram of PLL (frequency synthesizer) :
[Abolhasani, 2020]

## Slide 29: Phase Frequency detector
[Abolhasani, 2020]

## Slide 30: Actual PLL Output

## Slide 31: Phase Frequency detector

## Slide 32: Phase Frequency detector
[Divya, M, 2023]
Ffb < Fref
Result:
More up pulses to increase Ffb

## Slide 33: Phase Frequency detector
When the phase difference is near zero
[11]
UP pulse is very narrow to turn on the switch!

## Slide 34: Phase Frequency detector
UP pulse is very narrow to turn on the switch!
[11]
[Lee, 2002]

## Slide 35: Phase Frequency detector
Solution?
Extend the pulse with minimum overlap delay!
[11]
[Lee, 2002]

## Slide 36: Phase Frequency detector
[11]
Pulse extension
Old design
Pulse width is too low
New design
Pulse width is sufficiently high

## Slide 37: Phase Frequency detector
Δtmin
A solution to Dead Zone
Delay chain in the Reset Path to increase pulse width

## Slide 38: Different Architectures of Phase Frequency Detector
[S. M. M. Ahsan, 2020]
[Azadmousavi, 2018]
[K. Zouaq, 2018]

## Slide 39: Charge Pump
MOSFET Representation

## Slide 40: Charge Pump
Actual Circuit
Model Circuit
[S. M. M. Ahsan, 2020]
Current Ref.

## Slide 41: Charge Pump
Case #1: Up: High Pulse
Down: Low Pulse
[S. M. M. Ahsan, 2020]
Current Ref.
1
0
Vc
Loop Filter
0
1
Result:
VCO Voltage increases  Freq Increases

## Slide 42: Charge Pump
Case #2: Up: Low Pulse
Down: High Pulse
[S. M. M. Ahsan, 2020]
Current Ref.
1
0
Vc
Loop Filter
0
1
Result:
VCO Voltage Decreases
 Freq Decreases

## Slide 43: Filter Design
Can you guess the output for this RC filter?
To VCO

## Slide 44: Filter Design
I don’t want This!
Please HELP Me!!!!

## Slide 45: Filter Design

## Slide 46: Filter Design
Ahhh!!!!
Sweeeet!

## Slide 47: Frequency Divider
We can use DFF to divide frequency
[S. M. M. Ahsan, 2020]

## Slide 48: Frequency Divider

## Slide 49: Ring Oscillator
The more stages (n) there are, the lower the frequency will be.
t  the time delay for a single inverter
n  the number of inverters in the inverter chain
Caveat: The number of stages (n) MUST be odd

## Slide 50: Current Starved Ring Oscillator based VCO
Watch out for the start-up initial condition!!!!
Inverter
[S. M. M. Ahsan, 2020]
Vc

## Slide 51: Current Starved Ring Oscillator based VCO
NAND Inverter
[S. M. M. Ahsan, 2020]
[G. Korkian, 2017]

## Slide 52: Whole PLL

## Slide 53: Layout of the Whole PLL

## Slide 54: Layout of the Whole PLL

## Slide 55: Layout of the Whole PLL

## Slide 56: PLL Output

## Slide 57: Frequency across PVT

## Slide 58: Duty Cycle across PVT

## Slide 59: Step by Step Design Guide of PLL in Cadence

## Slide 60
Building Block of a PLL
A PLL primarily consists of 5 basic components
  Phase Frequency Detector (PFD): Ve ∝ φer
  Charge Pump (CP): Icp ∝ Ve
  Loop Filter: Vc ∝ Icp and filters out the high-frequency components
  Voltage Controlled Oscillator (VCO): Fout ∝ Vc
  Frequency Divider: Divide the output freq (Fout) to generate the feedback signal
Fig. Block diagram of a PLL [1]

## Slide 61: Features of the Designed PLL
Frequency Generation Range: From 200 MHz to 1.6 GHz.
Supply Voltage: 1.2 V
Transistor type: Regular Vt (Threshold Voltage)
Settling Time and Average Power Consumption:
  SS: 873 ns and 110.5 uW
  TT: 715 ns and 163.4 uW
  FF: 507 ns and 215.3 uW

## Slide 62: Building Block of the PLL with Multiple Frequency Generation
Fig. PLL with multiple frequencies

## Slide 63: PFD Circuit
Fig. PFD Core Circuit
Fig. PFD Core Symbol
Fig. PFD Circuit Symbol
Fig. PFD Circuit

## Slide 64: PFD Layout
Fig. PFD Core
Fig. PFD Core Symbol
Fig. PFD Core Layout
Fig. PFD Core LVS Report

## Slide 65: PFD Layout
Fig. PFD Circuit
Fig. PFD Symbol
Fig. PFD Layout
Fig. PFD LVS Report

## Slide 66: Testbench for the PFD
Fig. PFD Testbench Setup

## Slide 67: Output of the PFD
FVCO appears earlier than FRef
FVCO appears later than FRef
Fig. PFD Output

## Slide 68
Let’s design the charge pump and loop filter
Fig. Charge pump and LF design

## Slide 69: Charge Pump and LF
Fig. Schematic of Charge Pump
Fig. LF schematic
Iref = 12 µA

## Slide 70: Testbench – CP & LF
Fig. Testbench of CP & LF
Two vbit modules to simulate the outputs from PFD
LF is connected at the output of the Charge Pump
Measure the voltage of CPOUT to validate the operation of the charge pump

## Slide 71: Test Result – CP & LF
Fig. Simulation result of CP & LF

## Slide 72
Let’s design the VCO
Fig. VCO design

## Slide 73: Voltage-Controlled Oscillator (VCO)
Fig. VCO schematic

## Slide 74: Testbench – VCO
Fig. VCO testbench

## Slide 75: Test Result – VCO
Fig. Frequency and Duty cycle vs Input voltage

## Slide 76
Let’s design the Frequency Divider with Programmable Feature
Fig. Frequency Divider with Programmable Feature

## Slide 77: Frequency Divider
Fig. Schematic of Frequency Divider

## Slide 78: Comparison between TSPC and Conventional DFF
Feature | TSPC DFF | Conventional DFF
Clocking | Single-phase | Two-phase or master-slave
Power Consumption | Lower dynamic, higher leakage | Higher dynamic, lower leakage
Speed | Faster | Slower
Design Complexity | Simpler (dynamic logic) | More complex (static logic)
Robustness | Less robust to noise, low-frequency issues | More robust across conditions
Area | Smaller | Larger
Since, we are designing relatively high frequency PLL, we will be using TSPC logic based DFF. Conventional DFF should also work!

## Slide 79: Freq Divider – Cont.
Fig. DFF symbol
Fig. TSPC-DFF Schematic

## Slide 80: Testbench – Freq Divider
Fig. Testbench of Frequency Divider

## Slide 81: Test Result – Freq Divider
Fig. Simulation Results of Frequency Divider

## Slide 82: 4:1 Multiplexer
Fig. Schematic of MUX
Fig. TG Based MUX

## Slide 83: Testbench - MUX
Fig. Testbench of MUX
Four vpulse modules to generate square waves with different frequencies
Select bits

## Slide 84: Test Result – MUX
Fig. Test result of MUX

## Slide 85: Schematic of the final PLL
Fig. schematic

## Slide 86: Testbench – PLL
Fig. PLL testbench

## Slide 87: Test Result – PLL
This PLL works for all three corners with 0.2 GHz, 0.4 GHz, 0.8GHz and 1.6GHz frequencies except for 0.8GHz SS corner.
Not locking

## Slide 88: Best of luck for your own design!
Thanks

## Slide 89: References
[1] A. Abolhasani, M. Mousazadeh, and A. Khoei, “A high-speed, power efficient, dead-zone-less phase frequency detector with differential structure,” Microelectronics Journal, vol. 97, p. 104719, Mar. 2020, doi: 10.1016/j.mejo.2020.104719.
[2] Pothina, C.K.; Singh, N.P.; Prasanna, J.L.; Santhosh, C.; Kumar, M.R. Design of Efficient Phase Locked Loop for Low Power Applications. Eng. Proc. 2023, 34, 14. https://doi.org/10.3390/HMAM2-14157
[3] P. Chen, J. Yin, F. Zhang, P. -I. Mak, R. P. Martins and R. B. Staszewski, "Mismatch Analysis of DTCs With an Improved BIST-TDC in 28-nm CMOS," in IEEE Transactions on Circuits and Systems I: Regular Papers, vol. 69, no. 1, pp. 196-206, Jan. 2022, doi: 10.1109/TCSI.2021.3105451
[4] S. M. M. Ahsan, T. Hassan, S. I. Hasan, N. Afroz and S. A. Raisa, "Design and Performance Analysis of A Low Power, Low Noise 1.6GHz Charge Pump Integer-N PLL in Different PVT Corners," 2020 11th International Conference on Electrical and Computer Engineering (ICECE), Dhaka, Bangladesh, 2020, pp. 190-193, doi: 10.1109/ICECE51571.2020.9393111.
[5] C. Zhang, T. Au and M. Syrzycki, "A high performance NMOS-switch high swing cascode charge pump for phase-locked loops," 2012 IEEE 55th International Midwest Symposium on Circuits and Systems (MWSCAS), Boise, ID, USA, 2012, pp. 554-557, doi: 10.1109/MWSCAS.2012.6292080
[6] A. Zaziąbł, "Low power 1 GHz charge pump phase-locked loop in 0.18 µm CMOS process," Proceedings of the 17th International Conference Mixed Design of Integrated Circuits and Systems - MIXDES 2010, Wroclaw, Poland, 2010, pp. 277-282
[7] N. Khalid and R. C. S. Chauhan, “Performance analysis of various charge pump topologies for PLL application,” in Lecture notes in electrical engineering, 2023, pp. 331–349. doi: 10.1007/978-981-99-0973-5_25
[8] Oscillator, Available: https://moodle.insa-toulouse.fr/file.php/60/content/rfc_oscillators.html
[9] Yoo, B., Madgavkar, A., Jones, B. A., Nadkarni, S., Facchetti, A., Dimmler, K., ... & Dodabalapur, A. (2006). Organic complementary D flip-flops enabled by perylene diimides and pentacene. IEEE electron device letters, 27(9), 737-739.
[10] Zhu, Wen-rui et al. “A 5.8-GHz Wideband TSPC Divide-by-16/17 Dual Modulus Prescaler.” IEEE Transactions on Very Large Scale Integration (VLSI) Systems 23 (2015): 194-197.
[11] Phase-Locked Loops, IIT Madras, Prof. Saurabh Saxena, Prof. Saurabh Saxena, available: https://nptel.ac.in/courses/108106184